HARDWARE:
The wiring diagram attached should be used. Hereafter, sensor packages will be referred to as either:
Series 1: Six MCP9808 temperature sensors in parallel (all on the same I2C bus).
Series 2: Four MCP9808 temperature sensors in parallel (all on the same I2C bus), and two SHT75 humidity sensors as shown on pinout.

(Facing SHT75:
Pin 1 (DATA) connects to CLK
Pin 2 (VCC) connects to 3v3
Pin 3 (GND) connects to GND
Pin 4 (SYSCLK) connects to data pin

ANY GPIO PIN SHOULD WORK WITH THE DATA PIN FOR THE sht_sensor LIBRARY.
NOTE THAT GPIO PINS 4, 5, 6, 7, 8 AND 15 WORK WITH THE SCLK PINS WITH THE sht_sensor LIBRARY.

SOFTWARE
Regardless of Raspbian distribution, do the following list of commands.

(Most commands require the prefix sudo – this is short for super-user-do, and is the command that allows the user to run programs/make modifications to the OS as a superuser (highest authority).

(apt stands for advanced packaging tool, and is a host of tools that allows installation of packages onto the linux-based operating system.)

To use I2C devices:

In terminal, type the following:
- sudo apt-get update
- sudo apt-get upgrade
- sudo apt-get install -y python-smbus
- sudo apt-get install -y i2c-tools
- sudo raspi-config
Follow the prompts to install i2c support.
Go to interface options, or advanced options.
Select the I2C option.
Select enable.
Restart the Pi.
To test I2C (and see which peripherals are connected) go into terminal and type:
sudo i2cdetect -y 1

In order to use the MCP9808 Device:
In terminal, type the following:
- sudo apt-get update
- sudo apt-get install build-essential python-dev python-pip python-smbus git
- sudo pip istall Rpi.GPIO
You must download the library to your home directory and install it:
- cd ~
- git clone https://github.com/adafruit/Adafruit_Python_MCP9808.git
- cd Adafruit_Python_MCP9808
- sudo python setup.py install

In order to use the SHT75 Device:
In terminal, type the following:
- cd~
- wget https://pypi.python.org/packages/source/r/rpiSht1x/rpiSht1x-1.2.tar.gz
- sudo gunzip rpiSht1x-1.2.tar.gz
- sudo tar -xvf rpiSht1x-1.2.tar
- cd rpiSht1x-1.2/
- sudo python setup.py install
- cd ..
- rm rpiSht1x-1.2.tar
- sudo rm -rf rpiSht1x

In order to use the plotting libraries:
In terminal, type the following:
- sudo pip install matplotlib
- sudo pip install numpy